## Slide 1: Advanced Testbenches
Lecture 2

## Slide 2: Up to now…
Manipulated DUT inputs from testbench
  “Stimulus only” testing
Observed output in waveforms
No automated checking
Ok for small number of inputs & outputs and in early stage of development
Problems arise in larger designs:
  Error prone
  Unmanageable with larger IO
  Not systematic
  Does not support random testing
  Slow
Notes: Analyse the output of a large memory block, or a stream of video data by eye?
We want defined systematic testing to ensure functionality and coverage.

## Slide 3: Verification In Industry
Standardised testbench structure
  ASIC verification: UVM (Universal Verification Methodology) structure via SV
Separation of testbench and test cases
  Testbench instantiations “Device Under Test” (DUT) or “Device Under Verification” (DUV)
  Test case provides stimulus for particular use-case / feature
  Test plan lists required testcases
Constrained randomisation
Automatic pass/fail derived from model of DUT
Coverage metrics used to ensure testing is sufficient
  100% coverage expected
  Types of coverage: toggle, condition, branch
Notes: Verification large part of chip design today
Very important in ASIC, cost of errors extremely high
Design complexity has greatly increased

## Slide 4: Designer Testing in Industry
Used by designer from very beginning of development process
Structure is more simple than full verification environment
Self-checking options:
  Software model producing “golden vectors”, use File IO methods for comparison
  Verilog model to compute expected output for given stimulus
  Directed testing with defined expected output
Key: Provide pass/fail results without needing to inspect waveforms
Log-file should be produced to record pass/fail per feature

## Slide 5: Example: Counter Test Plan
In-Class Whiteboard:
  Write up ideas for test plan for counter with…
    4-bit counter
    Enable pin
    Reset pin
    Up/Down pin

## Slide 6: Useful Testbench Constructs
Advanced testbenches will require using new features of Verilog
Note these features are primarily non-synthesizable, testbench only
Notes: Contrary to writing Verilog for design where we are directly describing the circuits we want to implement. For verification, we have no such restrictions. We can write procedural testbenches, and even use object oriented features of system Verilog in more advanced cases.

## Slide 7: Useful Testbench Constructs
Four loop constructs in Verilog:
  for, while, repeat, forever
Three time control constructs
  #, @, wait
System tasks for controlling simulation
System tasks for displaying text and variable values
File IO system tasks
Custom functions and tasks
Notes: # is a fixed delay
Wait is a conditional delay
@ is triggered

## Slide 8: for loop
for (initial_assignment;end_condition;step_assignment) begin
  procedural statement;
  procedural statement;
  …
end
Example: Initialise 16-word register bank
integer i;
…
for (i=0; i<16; i=i+1) begin
reg_file[i] = 8’(i);
end
Notes: What is 8’(i) doing?

## Slide 9: while loop
while (end_condition) begin
  procedural statement;
  procedural statement;
  …
end
Previous example redone as while loop:
integer i;
…
i=0;
while(i<16) begin
reg_file[i]= 8’(i);
i=i+1;
end
Notes: For example only, for loop should be done when number of iterations known (like C)

## Slide 10: repeat loop
repeat (number) begin
  procedural statement;
  procedural statement;
  …
end
Example repeat loop:
repeat(16) begin
count_en = 1;
#100;
count_en = 0;
#100;
end
Notes: Repeat stimulus pattern
Very useful when used in conjunction with tasks also

## Slide 11: forever loop
forever begin
  procedural statement;
  procedural statement;
  …
end
Example forever loop
initial begin
clk = 1’b0;
forever
#20 clk = ~clk;
end
Notes: Clock stimulus

## Slide 12: Useful Testbench Constructs
Four loop constructs in Verilog:
  for, while, repeat, forever
Three time control constructs
  #, @, wait
System tasks for controlling simulation
System tasks for displaying text and variable values
File IO system tasks
Custom functions and tasks

## Slide 13: Timing Control
Three different time control constructs:
Delay control
  #delay_time
Event control, edge sensitive
  @(event1, event2…)
Wait statement, level sensitive
  wait(boolean_expression)
  Waits for specific condition to become true
  Subsequent statements not executed until that condition filled, e.g.
  wait(counter == 4’d15) // waits until counter is 15
  … // then rest gets executed
Notes: NB Difference between event control and wait control
Also `timescale 1ns/1ps method (units / precision)

## Slide 14: Useful Testbench Constructs
Four loop constructs in Verilog:
  for, while, repeat, forever
Three time control constructs
  #, @, wait
System tasks for controlling simulation
System tasks for displaying text and variable values
File IO system tasks
Custom functions and tasks

## Slide 15: System Functions and Tasks
System-related operations
  Simulation control and file access
  Begin with $, e.g. $monitor
  Full list in Verilog-2001 reference book
  We’ll use
    $finish, $stop,
  Also:
    $display, $write, $strobe, $monitor
Notes: Finish vs stop

## Slide 16: Display Tasks
$display
  $display(format_string, arg,arg,…);
  $display(“At %d; signal x = %b”, $time, x)
    At 5100; signal x = 00111100
$write same as display but no new line
$strobe similar syntax but executes later
  Executes at end of current simulation time step
$monitor
  Prints updated values at end of time step

## Slide 17: Rememer: Verilog Simulator Event Queue

## Slide 18: Demo: Printing to Tcl Console
reg [3:0] a,b;
integer i;
initial begin
$monitor( "monitor a:%h b:%h @ %0t" , a, b, $time);
for(i=0; i<4; i=i+1) begin
$strobe( "strobe a:%h b:%h @ %0t" , a, b, $time);
$display( "display a:%h b:%h @ %0t" , a, b, $time);
case(i)
0 : a = 4;
1 : b = 1;
2 : begin end // Do nothing
3 : {a,b} = 9;
endcase
$display( "display a:%h b:%h @ %0t", a, b, $time);
#1;
end
end
Notes: Take 5 mins to decide what order you expect outputs to get printed, what values and when, then will run a simulation and use the debugger to check this
Tcl console output from example…
Load example, show code for several minutes and ask what order the statements will be activated in
initial – what does this mean?
Note, also final in SV

## Slide 19: Useful Testbench Constructs
Four loop constructs in Verilog:
  for, while, repeat, forever
Three time control constructs
  #, @, wait
System tasks for controlling simulation
System tasks for displaying text and variable values
File IO system tasks
Custom functions and tasks

## Slide 20: File IO Tasks
Access external data files
Open file
  $fopen, e.g.
  Syntax: mcd_name = $fopen(“file_name”);
  Example: log_file = $fopen(“logfile.txt”);
  mcd: 32b int with one NZ bit for file, zero on failure
  OR combination of mcd can be used to output to multiple files
Close file
  $fclose, e.g.
  Syntax: $fclose(mcd_name);
  Example: $fclose(log_file);
Write to file with
  $fdisplay, $fwrite, $fstrobe, $fmonitor

## Slide 21: File IO Tasks
Two system tasks which don’t use $fopen:
  $readmemh
  $readmemb
Assume external file content is stored as a memory array.
  Read the array into a variable, mem_var
    $readmemb(“file_name”, mem_var);
    $readmemh(“file_name”, mem_var);
  $fscanf
  Read in one line at a time
  Provides text format flexibility,
  Requires $fopen, $fclose and check for $feof
Notes: Fscanf will return the number of assignments it has made based on what it has read in for that line
If attempts to read past the end of the file then feof will go high
Should have while loop checking that fscanf returns high, var assigned, and checking that feof isn’t high. Would have $finish after get $feof to end simulation.

## Slide 22: File Format For $readmemb
  reg [3:0] v_mem [0:7]; $readmemb(“vector.txt”, v_mem);
Just contains text as:
  00_00
  01_00
  01_11
  10_10
  10_00
  11_11
  11_01
  00_10
Notes: Note, this reads in full file as single variable in testbench… What if vector is very long?

## Slide 23: Useful Testbench Constructs
Four loop constructs in Verilog:
  for, while, repeat, forever
Three time control constructs
  #, @, wait
System tasks for controlling simulation
System tasks for displaying text and variable values
File IO system tasks
Custom functions and tasks

## Slide 24: Custom Functions and Tasks
Useful in testbenches
  Can be synthesizable in the right conditions
Improve readability of code
Avoid code repetition
Examine syntax now…

## Slide 25: User-Defined Functions
Takes one or more inputs
Returns single output
Completes in single time step
  No #, wait, @ allowed
Can call another function
Returns a value which may be used in an expression
Can be synthesizable if computed at compile time
  e.g. calculate vector width from parameter

## Slide 26: Function Syntax
// Function definition
function result_type func_id (input_arg);
statements;
endfunction
Difference in SystemVerilog, Verilog-2001 requires begin-end pair inside function-endfunction
Statements inside need to assign value to func_id (return variable name)
  Void type may be used if no return value desired

## Slide 27: Example Use of Function
// Listing 7.16
module eq2_function (input wire [1:0] a, input wire [1:0] b, output reg aeqb);
// Local variables
reg e0, e1;
// Combinational logic
always @(*) begin
#2 e0 = equ_fnc(a[0], b[0]);
#2 e1 = equ_fnc(a[1], b[1]);
aeqb = e0 & e1;
end
// function definition
function equ_fnc(input i0, input i1);
equ_fnc = (~i0 & ~i1) | (i0 & i1);
endfunction
endmodule
Notes: Chu book
Model of desired behaviour
Non-synthesizable verilog, quickly write and get value of expected result, compare and report in your log file
#2 to mimic clock cycle, not real hardware!
No output type on function, assumed to be 1 bit

## Slide 28: User-Defined Tasks
More flexibility than function
Can take zero or more inputs
Multiple values can be returned through output or inout arguments
Allows time control constructs, may execute in non-zero simulation time
Can call other tasks as well as other functions

## Slide 29: Task Syntax
// Task definition
task task_id (arg);
statements;
endtask
SV removes begin-end inside task-endtask
No need to assign a value to task_id, all inputs, outputs defined in arg
Notes: Should be very comfortable with task and function definitions, should know their differences in requirements and usage

## Slide 30: Example Use of Task
// Listing 7.15
module eq2_task (
input wire [1:0] a,
input wire [1:0] b,
output reg aeqb
);
// Local Variables
reg e0, e1;
// Combinational Logic
always @ (*) begin
equ_tsk(2, a[0], b[0], e0);
equ_tsk(2, a[1], b[1], e1);
aeqb = e0 & e1;
end
// task definition
task equ_tsk (
input integer delay,
input i0, i1,
output eq1
);
#delay eq1 = (~i0 & ~i1) | (i0 & i1);
end
endmodule
Notes: Not synthesizable

## Slide 31: Example Use of Function
// Listing 7.16
module eq2_function (input wire [1:0] a, input wire [1:0] b, output reg aeqb);
// Local variables
reg e0, e1;
// Combinational logic
always @(*) begin
#2 e0 = equ_fnc(a[0], b[0]);
#2 e1 = equ_fnc(a[1], b[1]);
aeqb = e0 & e1;
end
// function definition
function equ_fnc(input i0, input i1);
equ_fnc = (~i0 & ~i1) | (i0 & i1);
endfunction
endmodule
Notes: Comparison:
Time of execution
Usage of time delay / wait constructs
Return values

## Slide 32: Task vs Function: Comparison
Task | Function
May execute on non-zero simulation time | Must execute on zero simulation time
May have delay, event or timing control constructs | Can’t use time control constructs as it executes on zero simulation time
Cannot return a value | Always return a single value
Pass values (can be multiple) through output or inout arguments | Cannot have output or inout arguments
Can enable other functions and tasks | Can enable other functions but not tasks
Can have input, output or inout | Must have at least one input. Cannot have output or inout